## Slide 1: AdaptiveFlow: An Actor-based Framework to Design Flow Management Systems

## Slide 2: Flow Management Systems
Warehouse Management System
Transporting Shuttles in a Closed Environment
Public Transportation System
Airport and Airspace Systems

## Slide 3: Challenges
Performance
Safety
Adaptation

## Slide 4: Common Flow Pattern
Points of Interest
loading stations
wheel loader
airport runways
metro stops
parking stations
fuel stations
…
Machines
robots
haulers
airplanes
trains
buses
shuttles
…
Assets
packages
stones
passengers
materials
animals
letters
…
MOVING
TRANSPORTING
BETWEEN
Environments
warehouse aisles
urban roards
airport tracks
metro tunnels
airspace
quarry roads
…

## Slide 5: AdaptiveFlow Framework
Adaptation Policies
Topology
Env.
Cnfg.
More experiments?
Change input
No
Yes
Record results
Timed Rebeca model
Model generation
Performance Evaluation
Safety verification
State space
(Timed Transition System)

## Slide 6: Rebeca: The Modeling Language
Rebeca: Reactive object language
  Based on Hewitt actors
  Concurrent reactive objects (OO)
  Java-like syntax
Communication:
  Asynchronous message passing
  No explicit receive
Computation:
  Take a message from top of the queue and execute it
  Event-driven
Timed Rebeca (TRebeca):
  An extension of Rebeca with timing primitives

## Slide 7: Rebeca: Tool Support
Project editor
http://www.rebeca-lang.org/
Model and Property editor
Model checking result view

## Slide 8: Actor Templates in AdaptiveFlow
Eulerian
Lagrangian
Eulerian:
  segments as actors
  moving objects as messages
Lagrangian:
  moving objects as actors
    actors have some global view
    helping in autonomous decision making

## Slide 9: Adaptive Policies in AdaptiveFlow
Policy 1: wait & try again later
0_2 > 0_3 > 1_4 > 1_5 > 1_6
0_2 > 0_3 > 1_4 > 1_5 > 1_6
Policy 3: Re-route
0_2 > 0_3 > 1_4 > 1_5 > 1_6
0_2 > 0_3 > 0_4 > 0_5 > 1_6
Policy 2: overpass segment
0_2 > 0_3 > 1_4 > 1_5 > 1_6
0_2 > 0_3 > 0_4 > 0_5 > 1_5 > 1_6

## Slide 10: Safety & Performance Analysis
Safety Verification
Deadline misses
Deadlock
Starvation
Fuel outage
Collisions
Wrong movements
Performance Evaluation
Consumed Fuel
Emitted CO2
Transported Material
Operational time
Travel Distances
Starvation situation

## Slide 11: Optimization
Experiments
Moving PoIs within the environment
Change configuration of machines
Change sequence of tasks to execute
Change environment features
Try different Adaptive Policies
...
Configurations Comparison
The best position for the PoIs
Which is the most productive machine
Optimize tasks scheduling
Update the environment configuration
Select the most suitable Policy
...
GOAL
Essentially, all models are wrong, but some are useful.

## Slide 12: Project Team
Marjan Sirjani
MDH
Stephan Baumgart
MDH, Volvo CE
Torbjörn Martinsson
Volvo CE
Ali Jafari
RU
Giorgio Forcina
MDH
Ali Sedaghatbaf
MDH
Jonn Lantz
Volvo Cars
Ehsan Khamespanah
RU

## Slide 13: Publication
An Actor-based Design Platform for System of Systems
Authors: Marjan Sirjani, Giorgio Forcina, Ali Jafari, Stephan Baumgart, Ehsan Khamespanah, Ali Sedaghatbaf

## Slide 14: Sponsors
This work is financed by: